## Slide 1: Re-visioning for Individual Weapons Qualification (IWQ)
TC 3-20.0 Integrated Weapons Training Strategy (IWTS)
TC 3-20.40 Training and Qualification – Individual Weapons
U.S. Army Reserve Marksmanship Program
www.usar.army.mil/ARM ArmyReserveMarksman.info

## Slide 2: AAR Review of Previous Range
How do you feel it went?
What steps were you required to take prior to firing a single round?
Other factors that were put in place that contributed to success?
Notes: All range cadre had a binder with targeted doctrine experts to support executing their role to standard.
Everyone took an assessment to
Phase Gates:
Pass assessment (weapon and optic specific)
Bore sight optic
Opportunity for 1:1 coaching PRIOR to zeroing
Load your own magazines – confirming the correct number of rounds. Magazine and rounds were not damaged.
When zeroing, coaches all had a binder (at least initially). Coaching protocol was available at almost every lane.
Coaches were SELECTED rather than just assigned. Rank does not equate to competence. Pick people who can calmly articulate what to do.
Ongoing AAR binders at key locations to capture solder feedback as things were happening, with range leadership monitoring the binders though out the day.

## Slide 3: Goals
Conceptualize changes
Synergize preparation efforts among leadership
Allow Soldiers down to the E-2 level to take initiative and assist in the execution of the range

## Slide 4
Example Responsibilities for each role are in
TC 3-20.40 Chapter 4

## Slide 5: Example Range Walk Through
Notes: Phase gates enforced – Must pass written exam before bore sighting. Must bore sight before grouping and zeroing.
Opportunity to ask questions at each station.
Soldiers load their own ammo.
One set of soldiers acts as lane safeties. This primes them for the marksmanship mindset, as well as allows for good flow, and ensures a soldier doesn’t get left out on the line for the entire day.
Frees up the most knowledgeable soldiers to evaluate issues.

## Slide 6: Current Qualification Walk Through
Notes: Four Firing phases,
Prone unsupported, prone supported, kneeing supported, standing supported 4 10 round mags
Six Tables of training
PMI&E- Must take written and hands on test to progress
Pre Live Fire Simulations- RST
Drills
Basic- First live fire table (zeroing)
Practice- executing qualification course to prepare for actual Qualification
Qualification

## Slide 7: You should have a weapon and optic assigned on the Company MAL.
Resource: Creating a MAL
Notes: New qualification for Rifle.
Same course of fire for M249AR.
2019 was the first Ramp Up in quality execution. 2020 was obviously canceled.
TC 3-20-0 Articulates the
Sources: TC 3-20.40 Para 1-21

## Slide 8: Understanding the Individual Weapons Training Strategy
Run
Walk
Crawl
Table 1
Preliminary Marksmanship Instruction & Evaluation (PMI&E)
0.5 Days
Table 2
Preliminary Live Fire Simulations (PLFS)
0.5 Days
Table 3
Drills
1 Day
Table 4
Group & Zero
0.5 Days
Table 5
Practice
1 Day
Table 6
Qualification
1 Day
Table 1
Table 2
Table 3
Table 4
Table 5
Table 6
Notes: Sources:
TC 3-20.0

## Slide 9
Notes: Sources:
TC 3-20.40 Table 10

## Slide 10
Hands on demonstration of tasks
Soldiers are evaluated:
  Written test
  Performance test using physical weapon
Verifies Soldier’s ability to:
  Perform critical tasks
  Apply immediate and remedial action
  Employ the weapon safely
Trainers - dig into DOCTRINE, not just prior experience.
Use T&EOs to evaluate soldiers on tasks... not just death by PowerPoint.
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Table 1
Preliminary Marksmanship Instruction & Evaluation (PMI&E)
This table is a REQUIREMENT before any live-fire event - TC 3-20.0 Para 3-5
Notes: Sources:
TC 3-20.0 Para 3-5

## Slide 11
Reinforces Tasks:
  Weapons and Equipment Check
  4 firing positions
  Clear Malfunctions
  Load, Reload, Unload and Show Clear
CBRN & Night Fire
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Table 2
Preliminary Live Fire Simulations
(PLFS)
This table is a REQUIREMENT before any live-fire event - TC 3-20.0 Para 3-5
Observe shooter. Provide Feedback.
Notes: Sources:
TC 3-20.0 Para 3-6 and 3-7

## Slide 12
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Table 3
Drills
See Appendix D in the Training Circular for your weapon.
Hands on training – Soldiers need their weapon and optic.
  Use training aids
    Blank ammo
    Dummy ammo
Tasks Trained and Evaluated:
  Sling/Unsling
  Fight Down (Standing – Kneeling – Prone)
  Fight Up (Prone – Kneeling – Standing)
  Go-To-Prone (Standing to Prone)
Tasks Reinforced:
  Weapons and Equipment Check
  Load-Reload-Unload and Show Clear
  Clear Malfunctions
  4 Firing Positions
Notes: Sources:
TC 3-20.0 Para 3-8

## Slide 13
Table 3
Drills
Table 1 PMI&E

## Slide 14
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Table 4
Group & Zero
This table is a REQUIREMENT before any live-fire event - TC 3-20.0 Para 3-5
Notes: Sources:
TC 3-20.0 Para 3-9 and 3-10

## Slide 15
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Confirm zero at distance – Targets in “bob” mode.
Last chance to tweak technique before qual.
Table 5
Practice
Notes: Sources:
TC 3-20.0 Para 3-11 and 3-12

## Slide 16: If a Soldier is not able to hit targets during Table 5 (Practice), should they advance to Table 6 (Qualification)? NO! Retrain as needed until they can achieve a sufficient hit rate.

## Slide 17
Run
Walk
Crawl
Table 1 PMI&E
Table 2
PLFS
Table 3
Drills
Table 4
Group & Zero
Table 5
Practice
Table 6
Qual
Table 6
Qualification
Notes: Sources:
TC 3-20.0 Para 3-13

## Slide 18
New Qualification in Action

## Slide 19
What changes did you notice from the old qual?

## Slide 20
Lane Safety – Watch the shooter...Not the targets
Lane Safeties may not call out targets, or give reminders to change positions, or magazines during Qual.
What do you think this is?

## Slide 21: Creative Execution Tables 1-3

## Slide 22: Creative Execution Tables 4-6

## Slide 23
Same Range & Target exposures.
Auto Rifle issued more ammo.
Notes: Source: TC 3-20.40 Table 1-13

## Slide 24
What if I fail to qualify on my first attempt?
Retrain - Do NOT just refire!
Multiple attempts can be made, but MARKSMAN Badge is the highest level awarded.
May attempt to re-qualify above MARKSMAN Badge after 45 days.
DA Photo and Promotion points limited to MARKSMAN Badge
Why? “This provides a better commander assessment on the overall proficiency of their Soldier's and effectiveness of past Unit Training Plans.” TC 3-20.40 Para 1-75
Notes: Sources:
TC 3-20.40 Para 1-73 to 1-75

## Slide 25: What if I have a Malfunction during Qual?
Weapons Malfunction?
Continue Firing
Immediate Action
Fixed?
Remedial Action
Fixed?
Weapon Needs Replacement/ Repair?
OIC Grants Refire
Yes
No
No
No
Yes
Yes
Yes
Soldier accepts score. Potential Qual Failure.
No
It is critical the soldier understands the importance of maintaining their weapon, magazine, and other equipment to the highest standard. – TC 3-20.0 Para 4-87

## Slide 26: Additional Notes on Malfunctions
Target failure – OIC may grant a refire. Soldier must redo entire qual course of fire.
Non-Mission Capable (NMC) Weapon – Determined by OIC directed inspection. Verified fault according to Technical Manual. Not due to fault of the Soldier. Requires armor support or higher.
If Soldier requires new weapon, they must group, zero, and confirm at distance before re-attempting qualification.
Notes: TC 3-20.0 Para 8-44

## Slide 27
Must be authorized by 1st General Officer.
Only extends previous qualification.
Can only be used once in a 24 month period.
Can’t we just do the ALT-C Qual?
See 3-20.40 Table 1-77 for more details.
Notes: Source: 3-20.40 Table 1-77

## Slide 28
TC 3-20.0 Chapter 2 – Month by month example checklists of what to complete

## Slide 29: Next Steps
Read through AAR from previous range
Assign all Soldiers a primary and secondary role.
Instructors dig into doctrine in prep for PMI
Squad and Platoon leadership
  Develop Evaluation for M4, Optics, and M9
  Familiarize and plan to evaluate your soldiers on Drills
Update MAL to align with range roaster
PMCS assigned weapons, optics, and magazines
Update OIC, NCOIC, RSO, and tower books

## Slide 30: Additional Resources
Rifle IWQ Failure Cascade Series
  Failure #1: Quick PMI
  Failure #2: Bad Shot Process and Drills Validation
  Failure #3: Wrong Zero Target
  Failure #4: Not Using Optics
  Failure #5: Inability to Group
  Failure #6: Bad Zero
  Failure #7: Bad Target Presentations

## Slide 31
Army Reserve Marksman Newsletter
The Changing Face of Rifle Qualification (Page 34)
Entering New IWQ into DTMS
Kneeling Position
Weapons Up and Down Range?

## Slide 32: Rifle Videos
M150 RCO
M68 CCO

## Slide 33
Weapon Malfunctions
Notes: Most common malfunctions are shooter induced. SPORTS will clear most shooter induced malfunctions
Failure to extract is cleared by mortaring the weapon or slamming the stock on the ground or your knee
Failure to eject is prevented by good weapon cleaning practices.

## Slide 34
Notes: Four Phases of M4 Qualification
First phase starts standing and firing at the first target in a standing unsupported position, then transitioning to a prone unsupported position.
Second is prone supported
Third is kneeling supported
Fourth is standing supported
To prepare soldiers should learn and use the tactical reloading drill, as the qualification has no break periods in between phases of the positions.
Use dummy cartridges drills to practice weapon malfunctions
The fight up drill is the best drill to practice qualification

## Slide 35
Notes: Course of Fire & Explanation
The new army rifle qual consists of using 4 10 round mags in one firing iteration covering prone supported and unsupported. As well as both kneeling and standing supported. The grading has been modified as well. You are still only required a 23 out of 40 to pass however there is a new lowest grade of “qualified”

## Slide 36
Full Course of Fire for Home Station Training
Notes: Qualification - Range Only
Target pop up demonstration

## Slide 37
Notes: Barricade simple rules:
Always get straight back behind the rifle for natural aim
Get as many points of contact as possible
Maintain barrel awareness
Utilize corners of barricades for maximum stability
Kneeling:
Don’t rest barrel on the barricade
Rest elbow on knee, don’t depend entirely on the barricade for stability

## Slide 38
Notes: Square your shoulders and hips on the barricade
Flat palm the barricade and keep your rifle snug using your thumb
Step back from the barricade to reload
Maintain good elbow knee contact while shooting kneeling supported

## Slide 39
Notes: Basic aim adjustment for targets at different ranges

## Slide 40
Notes: A minute of angle is an angular relation In regards to sights. 1 inch at 100 is 1 MOA.
1 click on M4 front sight is ¾ MOA 1 click on M16 is ½ MOA
The M68 (red dot) is not magnified and 1 click is ½ MOA
The ACOG is 4x magnification 1 click is 1/3 MOA on the internal knob and ½ MOA on the external

## Slide 41
Notes: General Practice for zeroing on Iron sights using a 25/300m zero
Use 5 shot groups and follow the instructions on the target

## Slide 42
Notes: Maintain the tip of the front sight to the desired target centered on the rear aperture
Look at the front sight post and not the target.
Wherever you look on the tip of the front sight post should be the same to maximize consistency.
Get a high firm grip up on the pistol grip and constantly keep your finger on the trigger, holding it to the rear as the trigger fires, do not flinch or remove finger from the trigger. This will reduce spread.

## Slide 43
Notes: When standing square your shoulders and hips while bending you knees and waist slightly
When kneeling place your elbow in your thigh or your tricep on you knee never place your elbow to your knee
When kneeling you can sit on your heel or foot
While prone you may rest the rifle on the mag if comfortable for you
Pivot your hips while prone

## Slide 44
Notes: Practice good workspace grip while loading the magazine and checking for malfunctions.
When unloading, remove the magazine and pull the charging handle 3 times to ensure the weapon is clear.

## Slide 45
Notes: Check and Stock wield
When shooting standing unsupported use for points of contact foregrip, pistol grip, stock,and face

## Slide 46
Notes: Notice how targets can pop up three at a time, quickly locating the targets will be vital.
Four firing positions mean not only reloading quickly in between the positions but also moving into the firing positions and looking down range quickly for the targets.
Malfunctions must be quickly corrected because the qualification is continuous.

## Slide 47
Notes: Practice Qual POV
Another video demonstration, this time from pov

## Slide 48
Notes: The hammer of the trigger group falls striking the firing pin held in the center of the bolt and bolt carrier group which strikes the primer of the chambered cartridge. The primer detonates igniting the powder charge in the cartridge propelling the projectile forward and down the barrel, chamber pressure is in the range of 50,000 PSIA. As the projectile passes the gas port located on the lower side of the barrel (at the front sight block) a small portion of gas from combustion of the powder in the cartridge is directed into a gas tube that runs back to a small blocked tube on the bolt carrier group. The gas forces the bolt carrier group back against the buffer and buffer spring. As the bolt carrier group moves aft, the bolt rotates and unlocks from the lugs of the chamber. By this time the gas pressure in the barrel has dropped to nearly atmospheric pressure as the projectile leaves the barrel. All remaining actions are the result of the gas impinging on the blocked tube on the bolt carrier group and the resistance of the buffer and spring. F=MA roughly applies. The bolt unlocks, and moves rapidly backwards, pulling the spent cartridge case from the chamber. As it travels back the bolt telescopes to full extension as the carrier passes the hammer re-cocking the hammer and trigger group, and as it reaches nearly full extension aft, the ejector kicks the expended cartridge to the right and out of the action. The buffer spring now forces the bolt carrier group forward. The lower bolt edge strips a fresh cartiridge from the magazine moving it forward and upward along the chamber feed ramp into the chamber, the bolt following and engaging the cartridge base. As the cartridge seats in the chamber the bolt continues forward telescoping inwards. The lugs on the bolt enter the matching chamber notches and as the bolt ends forward travel, rotates right, locking the chamber.
In semi-automatic mode the next squeeze of the trigger repeats the cycle. In burst mode the trigger group uses a clockwork like mechanism to permit three full cycles of the sequence above before the hammer is locked in the cocked position, requiring another squeeze of the trigger to fire another burst. Fully automatic fire which is only availiable on M16, M16A1 and some M4 Carbine models, when selected, allows the cycle to continue until the trigger is released (let up on) or the weapon expends all ammunition in the magazine.
The M16 and variants ARE NOT the AR-15 and variants available to civilians in the US. The M16 is a select fire (semi, burst, full automatic) weapon which only those manufactured before 1986 may be possessed by civilians under significant restrictions and costs. Since the M16 / AR 15 design fires from what is called “closed bolt” it makes a poor fully automatic weapon.

## Slide 49: Pistol Videos
M18
M17
M9

## Slide 50: Grip and Manipulation
Notes: Grip and Manipulation

## Slide 51: Pistol Basics
Notes: Pistol Fundamentals

## Slide 52
Trigger Control Demonstration Drill
Notes: Trigger Control Demonstration Drill

## Slide 53
Notes: Drawing the M9

## Slide 54
Notes: Grip and Trigger Control of the M9

## Slide 55
Notes: Weapon Manipulation for the M9